## Slide 1: Locomotion Control
Module Specification

## Slide 2: Module Purpose
Control the locomotion system so that it responds to high level manoeuvre commands
Monitor locomotion to ensure those commands are being executed
Make actuator data available to modules that require it
Locomotion Control
Manoeuvre Demand
Actuator Demand
Actuator Telemetry
Actuator Telemetry

## Slide 3: Functional Architecture

## Slide 4: Locomotion capability
6 drive wheels, 4 corner wheels have steering capability
Limits manoeuvres to those where the vehicle’s centre of rotation lies along the normal to the middle wheels
This gives three possible manoeuvres:
Skid Steering “tank”
Ackerman “car”
Point Turn “turret”
Interesting paper: https://www.ri.cmu.edu/pub_files/pub1/shamah_benjamin_1999_1/shamah_benjamin_1999_1.pdf

## Slide 5: Skid Steering Definition
Two parameters to describe a skid steer manoeuvre:
  Curvature, [1/m]
  Rover body speed, [m/s]
In this configuration, the rover will drive in a circle, radius , around the centre of rotation
Wheels are not steered, instead both sides are driven at different speeds
The speed of the rover, , is limited by the max/min speed of rotation of the wheels
Wheels on the “outside” of the circle must turn faster than those on the “inside”

## Slide 6: Ackerman Definition
Two parameters to describe an Ackerman manoeuvre:
  Curvature, [1/m]
  Rover body speed, [m/s]
In this configuration, the rover will drive in a circle, radius , around the centre of rotation
Corner wheels steered to point towards the centre of rotation
The speed of the rover, , is limited by the max/min speed of rotation of the wheels
Wheels on the “outside” of the circle must turn faster than those on the “inside”

## Slide 7: Point Turn Definition
One parameter to define a “turn on the spot” manoeuvre:
  Rotation rate, [rad/s]
In this configuration, the rover will turn about its centre
Corner wheels are pointed at the centre of the rover
Rotation rate limited by speed of the wheels

## Slide 8: Input Specification
[GROUP DISCUSSION]

## Slide 9: Output Specification
[GROUP DISCUSSION]

## Slide 10: Internal Control Flow
[GROUP DISCUSSION]