## Slide 1: Phobos Autonomy
System Initial Concept

## Slide 2: Autonomy Levels
Level 1: Path following
  Autonomy Manger
  Trajectory Control
  Localisation
Level 2: Obstacle avoidance
  Level 1
  Perception
  Terrain Evaluation
  Path Assessment
Level 3: Full autonomy
  Level 2
  Path planning
This year
Next year
https://www.youtube.com/watch?v=ng-YrKmqCtM

## Slide 3: Locomotion capability
6 drive wheels, 4 corner wheels have steering capability
Limits manoeuvres to those where the vehicle’s centre of rotation lies along the normal to the middle wheels
This gives two possible manoeuvres:
  Ackerman for general driving
  Point turn for heading changes
The autonomy system therefore needs to output to lower levels:
  Manoeuvre type
  Manoeuvre parameters

## Slide 4: Ackerman Definition
Two parameters to describe any general driving manoeuvre the rover can perform:
  Curvature, [1/m]
  Rover body speed, [m/s]
In this configuration, the rover will drive in a circle, radius , around the centre of rotation
The speed of the rover, , is limited by the max/min speed of rotation of the wheels
Wheels on the “outside” of the circle must turn faster than those on the “inside”
Conversion of Ackerman demands into motor demands is done by Locomotion Control
Manual driving could use Ackerman demands as well (joystick X for speed, joystick Y for curvature)

## Slide 5: Point Turn Definition
One parameter to define a “turn on the spot” manoeuvre:
  Rotation rate, [rad/s]
In this configuration, the rover will turn about its centre
Rotation rate limited by speed of the wheels
Conversion of point turn demands into motor demands is done by Locomotion Control
In manual mode, secondary joystick can be used to demand rotation rate, but mode switching is required to lockout Ackerman demands when executing point turn

## Slide 6: Functional Architecture

## Slide 7: Modules

## Slide 8: Autonomy Manager
Manages execution of the entire autonomy stack
Accepts telecommands and decides which modules need to be activated for that task
Handles autonomy internal state, makes relevant states available to other modules
Manages cyclic execution (i.e. calls module processing functions at the right time and at the right rate)
Handles any fault events:
  Decides how to respond to faults from modules (stop rover, reprocess terrain, etc.)
Sends telemetry back to ground station

## Slide 9: Locomotion Control
Decodes Ackerman/point turn demands into actuator level demands
Controls actuators in closed loop to ensure targets are met:
  Speed
  Position
Monitors actuators for faulty behaviour:
  Actuator non-responsive (stopped)
  Actuator non-responsive (moving)
  Actuator stalled (stuck on rock?)
  Backdriving

## Slide 10: Trajectory Control
Outputs Ackerman/point turn demands that keep the rover on the path
Needs to know:
  Position
  Attitude
  Path to follow
Should keep the rover within m of the path (TBD)
If outside safe zone (fault):
  Stop rover
  Point turn towards path
  Drive onto path
  Realign with path and continue

## Slide 11: Localisation
Combine sensor inputs to estimate rover position and attitude
IMU provides acceleration and rotation tracking
  Noisy and drifty data
Actuator sensors provide wheel odometry data
  Cant account for rover slipping on sand, therefore drifts
Stereo cameras provide visual odometry:
  Track points across multiple frames
  Estimate motion between frames using tracked points
  Provides “truth” against the noisy, drifty IMU and wheel odometry
V/O at lower rate than other methods, must propagate IMU/Act data between V/O acquisition times

## Slide 12: Navigation
Based on ExoMars Nav system (right)
Generate navigation maps from stereo images
Path assessment:
  Determine if path provided by ground is safe (passes over safe terrain)
  Stop rover if unsafe, or divert around obstacle?
Path planning:
  Determine own path through terrain
http://robotics.estec.esa.int/ASTRA/Astra2015/Papers/Session%201A/96038_Winter.pdf